## Slide 1
MODULE-1
OVERVIEW OF MICROPROCESSORS
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
1
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 2
MODULE-1
2
  Introduction to Microprocessors
  8-bit /16-bit Microprocessor
  Overview of Intel Pentium, I (i3, i5, i7) Series Processor.
Overview of Microprocessors
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 3
INTRODUCTION TO MICROPROCESSOR
3
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 4
INTRODUCTION TO MICROPROCESSOR
A computer is a programmable machine that receives input, stores and manipulates data/information, and provides output in a useful format.
Basic computer system consist of a Central processing unit (CPU)/ Microprocessor (μP), memory (RAM and ROM), input/output (I/O) unit.
4
COMPUTER SYSTEM
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
Input Device
Output Device
Memory
Control Unit
ALU
Register Array
CPU/μP
BLOCK DIAGRAM OF A BASIC COMPUTER SYSTEM

## Slide 5
INTRODUCTION TO MICROPROCESSOR
A microprocessor is a controlling unit of a computer, fabricated on a small chip capable of performing Arithmetic Logical Unit (ALU) operations and communicating with the other devices connected to it.
Microprocessor is a Programmable, Clock driven, Register based, Electronic device that reads instruction from a storage device, takes the data from input unit and process the data according to the instructions and provides the result to the output unit.
    Programmable- Perform Different set operation on the digital data depending on the sequence of instructions supplied by the programmer.
    Clock Driven – Whole task is divided into basic operations, are divided into precise system clock periods.
    Register Based – Storage element
    Electronic Device – fabricated on a chip
5
MICROPROCESSOR
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 6
INTRODUCTION TO MICROPROCESSOR
The microprocessor follows a sequence: Fetch, Decode, and then Execute.
Initially, the instructions are stored in the memory in a sequential order.
The microprocessor fetches those instructions from the memory, then decodes it and executes those instructions till STOP instruction is reached.
Later, it sends the result in binary to the output port. Between these processes, the register stores the temporarily data and ALU performs the computing functions.
CPU must equipped with necessary resource. Important resources of CPU:
    Registers – to store the information temporarily
    ALU – to carryout Arithmetic and Logical operation
    Program Counter (instruction Pointer) – to point the next instruction to be executed
    Instruction decoder – to interpret the instruction fetched into the CPU
6
How does a Microprocessor Work?
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 7
INTRODUCTION TO MICROPROCESSOR
Instruction Set − It is the set of instructions that the microprocessor can understand.
Bandwidth/Data size − It is the number of bits processed in a single instruction.
Clock Speed − It determines the number of operations per second the processor can perform. It is expressed in megahertz (MHz) or gigahertz (GHz).It is also known as Clock Rate.
Word Length − It depends upon the width of internal data bus, registers, ALU, etc. An 8-bit microprocessor can process 8-bit data at a time. The word length ranges from 4 bits to 64 bits depending upon the type of the microcomputer.
Data Types − The microprocessor has multiple data type formats like binary, BCD, ASCII, signed and unsigned numbers.
7
MICROPROCESSOR – IMPORTANT TERMS
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 8
INTRODUCTION TO MICROPROCESSOR
Cost-effective − The microprocessor chips are available at low prices and results its low cost.
Size − The microprocessor is of small size chip, hence is portable.
Low Power Consumption − Microprocessors are manufactured by using metaloxide semiconductor technology, which has low power consumption.
Versatility − The microprocessors are versatile as we can use the same chip in a number of applications by configuring the software program.
Reliability − The failure rate of an IC in microprocessors is very low, hence it is reliable.
8
MICROPROCESSOR – FEATURES
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 9
INTRODUCTION TO MICROPROCESSOR
9
APPLICATIONS OF MICROPROCESSOR
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 10
INTRODUCTION TO MICROPROCESSOR
10
MICROPROCESSOR BASED TEMPERATURE MONITORING SYSTEM
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 11
EVOLUTION OF MICROPROCESSORS
11
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 12
EVOLUTION OF MICROPROCESSORS
1969 - The assignment: Nippon Calculating Machine Corporation approached Intel to design 12 custom chips for its new Busicom 141-PF* printing calculator.
The Intel solution: lntel designed a set of four chips known as the MCS-4.
    ROM(4001) - To support the custom applications programs
    RAM(4002) - For processing data
    Shift registers(4003) - For the input/output (I/O) port
    CPU(4004) - Central Processing Unit
1971- Era of integrated electronics: Intel purchased the rights from Nippon Calculating Machine Corporation and launched the Intel 4004 processor and its chipset in the November 15, 1971.
12
WORLD’S FIRST MICROPROCESSOR -
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
INTEL 4004

## Slide 13
EVOLUTION OF MICROPROCESSORS
13
WORLD’S FIRST MICROPROCESSOR -
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
INTEL 4004
INTEL 4004 IC
DIE VIEW OF INTEL 4004 IC
INTERAL VIEW OF BUSICOM 141-PF
BUSICOM 141-PF PRINTING CALCULATOR
MARCIAN "TED" HOFF
FEDERICO FAGGIN
MASATOSHI SHIMA
STANLEY MAZOR
INVENTERS OF INTEL 4004 MICROPROCESSOR

## Slide 14
EVOLUTION OF MICROPROCESSORS
We can categorize the microprocessor according to the generations or according to the size of the microprocessor:
First Generation (4 - bit Microprocessors):
  The first generation microprocessors were introduced in the year 1971-1972 by Intel Corporation. It was named Intel 4004 since it was a 4-bit processor.
  It was a processor on a single chip. It could perform simple arithmetic and logical operations such as addition, subtraction, Boolean OR and Boolean AND.
Second Generation (8 - bit Microprocessor):
  The second generation microprocessors were introduced in 1973 again by Intel.
  It was a first 8 - bit microprocessor which could perform arithmetic and logic operations on 8-bit words. It was Intel 8008, and another improved version was Intel 8088.
14
WORLD’S FIRST MICROPROCESSOR -
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
INTEL 4004

## Slide 15
EVOLUTION OF MICROPROCESSORS
Third Generation (16 - bit Microprocessor):
  The third generation microprocessors, introduced in 1978 were represented by Intel's 8086, Zilog Z800 and 80286, which were 16 - bit processors with a performance like minicomputers.
Fourth Generation (32 - bit Microprocessors):
  Several different companies introduced the 32-bit microprocessors, but the most popular one is the Intel 80386.
Fifth Generation (64 - bit Microprocessors):
  After 80856, Intel came out with a new processor namely Pentium processor followed by Pentium Pro CPU, which allows multiple CPUs in a single system to achieve multiprocessing.
  Other improved 64-bit processors are Celeron, Dual, Quad, Octa Core processors.
15
WORLD’S FIRST MICROPROCESSOR -
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
INTEL 4004

## Slide 16
EVOLUTION OF MICROPROCESSORS
16
EVOLUTION OF INTEL PROCESSORS (1)
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 17
EVOLUTION OF MICROPROCESSORS
17
EVOLUTION OF INTEL PROCESSORS (2)
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 18
EVOLUTION OF MICROPROCESSORS
18
HOW INTEL MANUFACTURES CHIPS
MODULE-1
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
https://www.youtube.com/watch?v=4oQoZF_KRCc

## Slide 19: THANK YOU