## Slide 1
MODULE-7
ARM Instruction Set
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
1
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 2
MODULE-7
2
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
ARM Instruction Set
ARM Instruction- data processing instructions, branch instructions, load store instructions, SWI Instruction, Loading instructions, conditional Execution, Assembly Programming.

## Slide 3
ARM INSTRUCTION SET
3
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 4
ARM INSTRUCTION SET
4
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
Load-store architecture
Conditional execution of every instruction
Possible to load/store multiple registers at once
Possible to combine shift and ALU operations in a single instruction
3-address instructions
2 or 3 operand field
Number representation: Hexa-0x, Binary-0b
The processor operations is illustrated using examples with pre- and post-conditions, describing registers and memory before and after the instruction are executed
PRE <pre-conditions>
<instruction/s>
POST <post-conditions>
FEATURES

## Slide 5
ARM INSTRUCTION SET
5
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
Load store instructions : LDR, STR
Data processing instructions
    Move instructions : MOV, MVN
    Barrel shift instructions : LSL, LSR, ASR, ROR, RRX
    Arithmetic instructions : ADD, ADC, SUB, SBC, RSB, RSC
    Multiply instructions : MUL, MLA
    Logical instructions : AND, ORR, EOR, BIC
    Comparison instructions : CMP, CMN
Branch instructions : B, BL
Conditional execution instructions : EQ, NE, CS, CC, MI, PL, VS, VC, HI, LS, GE, LT, GT, LE, AL
Software interrupts instruction
Status register transfer instruction
Coprocessor instructions
ARM Instruction Set (ARMv5E) Classification

## Slide 6
ARM INSTRUCTION SET
6
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
Load-store instructions transfer data between memory and processor registers or immediately load the value to registers.
There are three types of load-store instructions:
  Single-register transfer - used for moving a single data item in and out of a register
  Multiple-register transfer - enable transfer of large quantities of data
  Swap - allow exchange between a register and memory in one instruction
However, Single-Register Transfer instructions are most commonly used to perform load store operation.
1. LOAD STORE INSTRUCTIONS
Instruction | Meaning | Example | Operation
LDR | Load word into a register | LDR r0, =0x0000000f | r0 := 0x0000000f
 |  | LDR r0, [r1] | r0 := mem32[r1]
STR | Store word into a register | STR r0, [r1] | mem32[r1] := r0
 |  | STR r2, [r5], #8 | mem32[r5] = r2, r5 = r5 + 8
Syntax: <LDR|STR>{<cond>}{B} Rd,addressing1

## Slide 7
ARM INSTRUCTION SET
7
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
Data processing instructions are manipulate data within registers.
Move copies N into a destination register Rd, where N is a register or immediate value.
This instruction is useful for setting initial values and transferring data between registers.
If suffix S used on a data processing instruction, then it updates the flags in the CPSR.
2. DATA PROCESSING INSTRUCTIONS (a) MOVE INSTRUCTIONS
Instruction | Meaning | Operation | Example | Description
MOV | Move a 32-bit value into register | Rd=N | PRE r5=0x00000005, r7=0x00000008 MOV r7, r5 POST r5=0x00000005, r7=0x00000005 | Move r5 value into r7
MVN | Move the NOT of the 32-bit value into register | Rd=~N | PRE r5=0x00000005, r7=0x00000008 MVN r7, r5 POST r5=0x00000005, r7=0xFFFFFFFA | NOT r5 value then move to r7
Syntax: <instruction>{<cond>}{S} Rd, N

## Slide 8
ARM INSTRUCTION SET
8
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
A unique and powerful feature of the ARM processor is the ability to shift the 32-bit binary pattern in one of the source registers left or right by a specific number of positions before it enters the ALU.
This shift increases the power and flexibility of many data processing operations.
This is particularly useful for loading constants into a register and achieving fast multiplies or division by a power of 2.
Most data processing instructions can process one of their operands using the barrel shifter.
It is possible to directly specify the number of bits to be shifted in the instruction itself.
2. DATA PROCESSING INSTRUCTIONS (b) BARREL SHIFT INSTRUCTIONS

## Slide 9
ARM INSTRUCTION SET
9
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
2. DATA PROCESSING INSTRUCTIONS (b) BARREL SHIFT INSTRUCTIONS
Instruction | Meaning | Shift | Example
LSL | Logical Shift Left |  | PRE R2=0x00000030 MOV R0, R2, LSL #2 ; R0:=R2<<2 POST R0=0x000000C0, R2=0x00000030
LSR | Logical Shift Right |  | PRE R2=0x00000030 MOV R0, R2, LSR #2 ; R0:=R2>>2 POST R0=0x0000000C, R2=0x00000030
ASR | Arithmetic Shift Right |  | PRE R2=0x80000030 MOV R0, R2, ASR #2 ; R0:=R2>>2 POST R0=0xE000000C, R2=0x80000030
ROR | ROtate Right |  | PRE R2=0x00000031 MOV R0, R2, ROR #2 ; R0:=R2 rotate 2 POST R0=0x4000000C, R2=0x00000031
RRX | Rotate Right eXtended |  | PRE R2=0x00000031,C=1 MOV R0, R2, RRX ; R0:=R2 rotate 2, C POST R0=0x00000018,C=1,R2=0x00000031

## Slide 10
ARM INSTRUCTION SET
10
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
The arithmetic instructions implement addition and subtraction of 32-bit values.
2. DATA PROCESSING INSTRUCTIONS (c) ARITHMETIC INSTRUCTIONS
Instruction | Meaning | Operation | Example
ADD | Add two 32-bit values | Rd = Rn + N | PRE r1=0x00000005 ADD r0, r1, r1, LSL #1 ; r0=(r1<<1)+r1 POST r0=0x0000000F, r1=0x00000005
ADC | Add two 32-bit values and carry | Rd = Rn + N + C | PRE r1=0x00000005, C=1 ADC r0, r1, r1, LSL #1 ; r0=(r1<<1)+r1+C POST r0=0x00000010, r1=0x00000005
SUB | Subtract two 32-bit values | Rd = Rn - N | PRE r1=0x00000002, r2=0x00000001 SUB r0, r1, r2 ; r0=r1-r2 POST r0=0x00000001
Syntax: <instruction>{<cond>}{S} Rd, Rn, N
N is the result of the shifter operation

## Slide 11
ARM INSTRUCTION SET
11
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
2. DATA PROCESSING INSTRUCTIONS (c) ARITHMETIC INSTRUCTIONS
Instruction | Meaning | Operation | Example
SBC | Subtract with carry of two 32-bit values | Rd = Rn - N - !C | PRE r1=0x00000002, r2=0x00000001, C=0 SBC r0, r1, r2 ; r0=r1-r2-!C POST r0=0x00000000
RSB | Reverse Subtract two 32-bit values | Rd = N - Rn | PRE r1=0x00000002, r2=0x00000005 RSB r0, r1, r2 ; r0=r2-r1 POST r0=0x00000003
RSC | Reverse Subtract with carry of two 32-bit values | Rd = N - Rn - !C | PRE r1=0x00000002, r2=0x00000005, C=0 RSC r0, r1, r2 ; r0=r2-r1-!C POST r0=0x00000002
N is the result of the shifter operation

## Slide 12
ARM INSTRUCTION SET
12
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
The multiply instructions multiply the contents of a pair of registers and, depending upon the instruction, accumulate the results in with another register.
2. DATA PROCESSING INSTRUCTIONS (d) MULTIPLY INSTRUCTIONS
Instruction | Meaning | Operation | Example
MUL | Multiply two 32-bit values | Rd=Rm*Rs | PRE r1=0x00000002, r2=0x00000002 MUL r0, r1, r2 ; r0=r1*r2 POST r0=0x00000004, r1=0x00000002, r2=0x00000002
MLA | Multiply two 32-bit values and accumulate | Rd=(Rm*Rs)+Rn | PRE r1=0x00000002, r2=0x00000002, r3=0x00000005 MUL r0, r1, r2, r3 ; r0=(r1*r2)+r3 POST r0=0x00000009, r1=0x00000002, r2=0x00000002, r3=0x00000005
Syntax: MUL{<cond>}{S} Rd, Rm
MLA{<cond>}{S} Rd, Rm, Rs, Rn

## Slide 13
ARM INSTRUCTION SET
13
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
Logical instructions perform bitwise logical operations on the two source registers.
2. DATA PROCESSING INSTRUCTIONS (e) LOGICAL INSTRUCTIONS
Instruction | Meaning | Operation | Example
AND | Logical bitwise AND of two 32-bit values | Rd = Rn & N | PRE r1=0x0000002F, r2=0x00000005 AND r0, r1, r2 ; r0=r1&r2 POST r0=0x00000005
ORR | Logical bitwise OR of two 32-bit values | Rd = Rn ¦ N | PRE r1=0x0000002F, r2=0x00000005 ORR r0, r1, r2 ; r0=r1¦r2 POST r0=0x0000002F
EOR | Logical bitwise XOR of two 32-bit values | Rd = Rn ^ N | PRE r1=0x0000002F, r2=0x00000005 EOR r0, r1, r2 ; r0=r1^r2 POST r0=0x0000002A
BIC | Logical bit clear (AND NOT) | Rd = Rn & ~ N | PRE r1=0x0000002F, r2=0x00000005 BIC r0, r1, r2 ; r0=r1&~r2 POST r0=0x0000002A
Syntax: <instruction>{<cond>}{S} Rd, Rn, N

## Slide 14
ARM INSTRUCTION SET
14
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
The comparison instructions are used to compare or test a register with a 32-bit value.
They update the CPSR flag bits according to the result, but do not affect register content.
After the bits have been set, the information can then be used to change program flow by using conditional execution
Instruction | Meaning | Operation | Example | Description
CMP | Compare | CPSR flag sets as a result of Rn-N | PRE CPSR=nzcvqiFt_USER, r0=0x00000008, r9=0x00000008 CMP r0, r9 POST CPSR=nZcvqiFt_USER | Since r0-r9 result is zero, “Z” flag is SET
CMN | Compare negate | CPSR flag sets as a result of Rn+N | PRE CPSR=nzcvqiFt_USER, r0=0xA0000000, r9=0x80000000 CMN r0, r9 POST CPSR=nzCvqiFt_USER | Since r0+r9 result generate carry, “C” flag is SET
Syntax: <instruction>{<cond>} Rn, N
2. DATA PROCESSING INSTRUCTIONS (f) COMPARISON INSTRUCTIONS

## Slide 15
ARM INSTRUCTION SET
15
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
A branch instruction changes the flow of execution or is used to call a routine which forces the program counter (pc) to point to a new address.
Branch instructions allows programs to have subroutines, if-then-else structures, and loops.
3. BRANCH INSTRUCTIONS
Instruction | Meaning | Operation | Example | Description
B | Branch | PC=label | B forward …… forward …… | Branching forward
BL | Branch with Link | PC=Label LR=Address of the next instruction after BL | BL calc …… calc <subroutine code> MOV pc, lr | Branching but after executing it return from subroutine using link register copied to PC
Syntax: B{<cond>} label
BL{<cond>} label

## Slide 16
ARM INSTRUCTION SET
16
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
4. CONDITIONAL INSTRUCTIONS
A beneficial feature of the ARM architecture is that instructions can be made to execute conditionally.
In ARM state, all instructions are conditionally executed according to the state of the CPSR condition codes and the instruction’s condition field.
If the state of the C, N, Z and V flags fulfils the conditions encoded by the field, the instruction is executed, otherwise it is ignored.
There are 16 possible conditions, each represented by a two-character suffix that can be appended to the instruction’s mnemonic. In practice, 15 different conditions may be used.
For example, a Branch (B in assembly language) becomes BEQ for "Branch if Equal", which means the Branch will only be taken if the Z flag is set.

## Slide 17
ARM INSTRUCTION SET
17
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
4. CONDITIONAL INSTRUCTIONS

## Slide 18
ARM INSTRUCTION SET
18
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
4. CONDITIONAL INSTRUCTIONS
CMP r0, #0 ; if (x <= 0)
MOVLE r0, #0 ; x = 0;
MOVGT r0, #1 ; else x = 1;
Assume x is in R0. Compare R0 to 0. The next instruction MOVLE will be executed only if the compare returns less than or equal. Later, check for Greater than condition and execute MOVGT instruction.
CMP r0, #'A' ; if (c == 'A‘)
CMPNE r0, #'B' ; || c == 'B')
MOVEQ r1, #1 ; y = 1;
Assume A is in R0. Compare R0 to ‘A’ The next instruction CMPNE will be executed only if the compare returns Not Equal. They move ‘B’ into R0, then check for EQUAL condition for MOVEQ instruction execution.
CMP r0, #5 ; if (a == 5)
MOVEQ r0, #10
BLEQ fn ; fn(10)
Assume a is in R0. Compare R0 to 5. The next two instructions will be executed only if the compare returns EQual. They move 10 into R0, then call ‘fn’ (branch with link, BL)

## Slide 19
ASSEMBLY PROGRAMMING
19
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS

## Slide 20
ASSEMBLY PROGRAMMING
20
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
area sample, code, READONLY
entry
start
LDR r0, =0x00000005 ; N=5
ADD r2, r0, #1
MUL r3, r2, r0
MOV r3, r3, LSR #1
Stop B stop
END
Write an ARM assembly language program to compute sum of first “n” numbers using the formula [n(n+1)/2]. Assume “n” as 5.
EXAMPLE – 1

## Slide 21
ASSEMBLY PROGRAMMING
21
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
area sample, code, READONLY
entry
CODE32
start
LDR r0, =0x1111ffff ; LSB 32-bit 1st number
LDR r1, =0x11110000 ; MSB 32-bit 2nd number
LDR r2, =0x1111ffff ; LSB 32-bit 1st number
LDR r3, =0x11110000 ; MSB 32-bit 2nd number
ADDS r4, r2, r0 ; Add LSBs
ADC r5, r3, r1 ; Add MSBs with carry
Stop B stop
END
Write an ARM assembly language program to compute addition of two 64-bit number.
EXAMPLE – 2

## Slide 22
ASSEMBLY PROGRAMMING
22
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
area sample, code, READONLY
entry
start
LDR r0, =0x00000006 ; a
LDR r1, =0x00000005 ; b
CMP r0,r1
MOVLT r4, r1
MOVGT r4, r0
stop B stop
END
Write an ARM assembly language program to find the largest of two 32-bit numbers.
EXAMPLE – 3

## Slide 23
ASSEMBLY PROGRAMMING
23
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
area sample, code, READONLY
entry
start
LDR r0, =0x00000000 ; i
LDR r1, =0x00000001 ; j
MOV r2, #15 ; count=15
loop ADD r1,r1,r1 ; j=j+j
ADD r0,r0,#1 ; i++
CMP r2,r0 ; r2-r0
BGT loop ; i<15?
stop B stop
END
Write an equivalent ARM assembly language program for the “for loop function” given for(i=0;i<15;i++) {j=j+j}.
EXAMPLE – 4

## Slide 24
ASSEMBLY PROGRAMMING
24
MODULE-7
BECE204L – MICROPROCESSORS AND MICROCONTROLLERS
area sample, code, READONLY
entry
start
LDR r0, =0x00000003 ; a
LDR r4, =0x00000001 ; c
LDR r5, =0x00000002 ; d
MOV r1, #5 ; count=5
CMP r0,r1 ; r0-r1
MOVLT r2,#5 ; x
ADDLT r3,r4,r5 ; y=c+d
SUBGT r2,r4,r5 ; y=c-d
stop B stop
END
Write an equivalent ARM assembly language program for the “if else function” given if(a>5){x=5;y=c+d} else x=c-d
EXAMPLE – 5